## Slide 1
The Indo-French TRISHNA mission
Monitoring our ecosystems from space
Philippe Gamet (CNES), Bimal K. Bhattacharya (SAC), Jean-Louis Roujean (CESBIO), Gilles Boulet (IRD), Emmanuelle Autret (IFREMER), Ghislain Picard (IGE), Laure Roupioz (ONERA), Mark Irvine (INRAE), Sébastien Marcq (CNES), Corinne Salcedo (CNES), Philippe Maisongrande (CNES)
Thermal Remote Sensing Workshop
and LST_cci User Workshop 2024
Leicester, UK – Dec 2-4, 2024

## Slide 2
Outline
The water issue
TRISHNA mission design
Evapotranspiration

## Slide 3
Global warming +2deg by 2050
Impact on Carbon and water cycles
Extreme events: droughts, floods,
storms, fires
~+2 billions people by 2050
Pressure ↗ on energy and food
Pressure ↗ on transboundary basins
Population ↗ in fluvial & coastal zones
Biodiversity / pressure on the habitat
In Rivers, wetlands, coastal zones
Modified by dams (connectivity),
pollution (health)
Adaptation, mitigation Stakes
involving Science and Application levels in Economy, ecology, geopolitics, security…
Reliable metrics needed, homogeneous along time and on every scale from global to regional
Essential Agricultural Variables
 meet current and evolving policy drivers for agriculture
The water issue

## Slide 4
Rapid increase of water consumption
Trends in water use by sector (UNEP) (http://www.unep.org/dewa/vitalwater/article43.html)
70% of World water use is for agriculture
World water use
Source: World Bank, World Development Indicators, 2012
Agriculture
Industry
Towns and municipalities
!
Increasing scarcity and deteriorating quality of the water resource
The water issue

## Slide 5
Source: FAO
Check also: https://www.un.org/waterforlifedecade/scarcity.shtml
The water issue

## Slide 6
Water cycle

## Slide 7
Water cycle
=
Ground Water
Surface Water
Soil Moisture
+
+
Water Storage
Precipitation
EvapoTranspiration
Run-off
-
-
Q
P
E

## Slide 8
ISRO/CNES cooperation, launch 2026
5-year lifetime
TRISHNA Mission design

## Slide 9
ISRO/CNES cooperation, launch 2026
5-year lifetime
Design drivers: ecosystem stress and water use; coastal & inland waters
Ecosystem health, drought, fire
Solid Earth
Urban heat
Cryosphere
Water mgmt, agriculture
Coastal and inland waters
TRISHNA Mission design

## Slide 10
Global coverage land + coastal
  Continental surfaces
  Coastal areas 100 km from the coastline
  Coastal waters with bathymetry < 250m
  Closed seas + Mediterranean Sea
  Antarctica coastline
ISRO/CNES cooperation, launch 2026
5-year lifetime
Design drivers: ecosystem stress and water use; coastal & inland waters
Global coverage land + coastal
TRISHNA Mission design

## Slide 11
Average revisit (in days)
Global coverage land + coastal
TRISHNA Mission overview
ISRO/CNES cooperation, launch 2026
5-year lifetime
Design drivers: ecosystem stress and water use; coastal & inland waters
Global coverage land + coastal
3-day revisit
TRISHNA Mission design
Uncertainty on Daily Evapotranspiration induced by interpolation - Sunflower crops in Grosseto over 2 years
Typical temporal pattern of acquisitions over Grosseto for LANDSAT, TRISHNA, LSTM and SBG
Courtesy of Albert Olioso

## Slide 12
Average revisit (in days)
Global coverage land + coastal
TRISHNA Mission overview
ISRO/CNES cooperation, launch 2026
5-year lifetime
Design drivers: ecosystem stress and water use; coastal & inland waters
Global coverage land + coastal
3-day revisit, 60m ground resolution
TRISHNA Mission design
60 m
TRISHNA ground sampling over a typical agriculture landscape in French Brittany

## Slide 13
Average revisit (in days)
Global coverage land + coastal
TRISHNA Mission overview
ISRO/CNES cooperation, launch 2026
5-year lifetime
Design drivers: ecosystem stress and water use; coastal & inland waters
Global coverage land + coastal
3-day revisit, 60m ground resolution
Different observation angles, up to 38 deg
TRISHNA Mission design

## Slide 14
Average revisit (in days)
Global coverage land + coastal
TRISHNA Mission overview
Overpass time must cope with max sensitivity for flux estimation
Noon to 1PM LST  max accuracy on fluxes retrieval
Minimizing the sensitivity of LST measurement to overpass time
 1PM LST more suited to models with 30mn-1h time steps
 1PM LST minimizes impact of time differences (orbit)
ISRO/CNES cooperation, launch 2026
5-year lifetime
Design drivers: ecosystem stress and water use; coastal & inland waters
Global coverage land + coastal
3-day revisit, 60m ground resolution
Different observation angles, up to 38 deg
Overpass time : 12:30 PM & AM at Equator
TRISHNA Mission design

## Slide 15
Average revisit (in days)
Global coverage land + coastal
TRISHNA Mission overview
0.5µm 0.6 0.7 0.8 0.9 1µm 1.1 1.2 1.3 1.4 1.5µm 1.6
8µm 9µm 10µm 11µm 12µm
Spectral bands
ISRO/CNES cooperation, launch 2026
5-year lifetime
Design drivers: ecosystem stress and water use; coastal & inland waters
Global coverage land + coastal
3-day revisit, 60m ground resolution
Different observation angles, up to 38 deg
Overpass time : 12:30 PM & AM at Equator
VNIR-SWIR (7 bands) – LWIR (4 bands)
NeDT 0.2K at instrument output, AKA 0.5K
TRISHNA Mission design

## Slide 16
ISRO/CNES cooperation, launch 2026
5-year lifetime
Design drivers: ecosystem stress and water use; coastal & inland waters
Global coverage land + coastal
3-day revisit, 60m ground resolution
Different observation angles, up to 38 deg
Overpass time : 12:30 PM & AM at Equator
VNIR-SWIR (7 bands) – LWIR (4 bands)
NeDT 0.2K at instrument output, AKA 0.5K
Free & open data policy
Level 1: top-of atm reflectances & brightness temp.
Level 2: ground and water reflectances, Land and Sea Surface temperature, Land Surface emissivities, vegetation variables, albedo, daily evapotranspiration
TRISHNA Mission overview
0.5µm 0.6 0.7 0.8 0.9 1µm 1.1 1.2 1.3 1.4 1.5µm 1.6
8µm 9µm 10µm 11µm 12µm
Spectral bands
Level 1C
TOA reflectances x7 VNIR/SWIR bands
TOA radiances x4 LWIR bands
Cloud mask
Radiometrically and geometrically calibrated
Orthorectified and resampled on a uniform spatial grid (Sentinel-2 tiles, Copernicus DEM)
Level 2A
Land & Water Surface reflectances
LST, SST
LSE x4 LWIR bands
Cloud mask, TWVC, AOT
Level 2B
Vegetation variables, albedo
Daily Evapotranspiration
Level 3
Time series of daily evapotranspiration
x5 VNIR/SWIR bands
Distributed Products
TRISHNA Mission design

## Slide 17
ISRO/CNES cooperation, launch 2026
5-year lifetime
Design drivers: ecosystem stress and water use; coastal & inland waters
Global coverage land + coastal
3-day revisit, 60m ground resolution
Different observation angles, up to 38 deg
Overpass time : 12:30 PM & AM at Equator
VNIR-SWIR (7 bands) – LWIR (4 bands)
NeDT 0.2K at instrument output, AKA 0.5K
Free & open data policy
Level 1: top-of atm reflectances & brightness temp.
Level 2: ground and water reflectances, Land and Sea Surface temperature, Land Surface emissivities, vegetation variables, albedo, daily evapotranspiration
International collaboration (products, ATBDs, orbits, cal/val, campaigns)
TRISHNA Mission overview
0.5µm 0.6 0.7 0.8 0.9 1µm 1.1 1.2 1.3 1.4 1.5µm 1.6
8µm 9µm 10µm 11µm 12µm
Spectral bands
Land Surface Temperature Monitoring
Surface Biology and Geology
LSTM
SBG
(Launch: 2029)
(Launch: 2028)
International Workshop on High-resolution Thermal Infrared Earth Observation (ESRIN, May 2023)
TRISHNA Mission design

## Slide 18
ISRO/CNES cooperation, launch 2026
5-year lifetime
Design drivers: ecosystem stress and water use; coastal & inland waters
Global coverage land + coastal
3-day revisit, 60m ground resolution
Different observation angles, up to 38 deg
Overpass time : 12:30 PM & AM at Equator
VNIR-SWIR (7 bands) – LWIR (4 bands)
NeDT 0.2K at instrument output, AKA 0.5K
Free & open data policy
Level 1: top-of atm reflectances & brightness temp.
Level 2: ground and water reflectances, Land and Sea Surface temperature, Land Surface emissivities, vegetation variables, daily evapotranspiration
International collaboration (products, ATBDs, orbits, cal/val, campaigns)
Global coverage land + coastal
TRISHNA Mission overview
0.5µm 0.6 0.7 0.8 0.9 1µm 1.1 1.2 1.3 1.4 1.5µm 1.6
8µm 9µm 10µm 11µm 12µm
Spectral bands
Average revisit (in days)
TRISHNA Mission design

## Slide 19
Evapotranspiration
Evapotranspiration (ET) represents the largest water loss component of continental surfaces
 key variable to rationalize the use of water for irrigated agriculture
Objective: deliver a continuous time series providing every day the best possible estimate of the field-scale daily evapotranspiration
ET also needed for: drought monitoring, weather and crop yield forecasting
 TRISHNA inputs to compute ET: level 2A (LST, Emissivity) + level 2B (vegetation variables, albedo, fluxes)
ET (mm/day) 8 July 2008 from ASTER (resolution 100m)

## Slide 20
Lλ,TOA = L↑ + [ρλ.L↓ + ελ.B (T)] x tλ
At-sensor Radiance
Radiance from the atmosphere
Radiance leaving the Earth surface
=
+
Atmospheric Transmission
x
Radiative transfer equation in the atmosphere: TRISHNA Level 1C to level 2A
Radiative Transfer in the atmosphere and energy balance at the surface
Rn(T) = Rg.(1 – a) + ε.Ra – ε.σ.T4
Rn(T) = H(T) + LE(T) + G(T)
Net Radiation
Sensible Latent Ground
Surface energy balance: TRISHNA Level 2B
λ
λ
λ
Evapotranspiration
LEVEL 2
LEVEL 1
From Bonan, Science 2008
Surface energy fluxes

## Slide 21
Satellite Acquisition
Level 3
Product
Timeliness of evapotranspiration products
Healthy crop
Stomatal
Closure to limit water losses
Plant heating up
Detectable with TIR
Water supply
Stomata
re-opening
Reduced photosynthesis
Reduced dry matter production
Water deficit
Detectable with VNIR
Healthy crop
Stomatal
Closure to limit water losses
Plant heating up
Healthy crop

## Slide 22
Summary / Takehome messages
Evapotranspiration represents the largest water loss component of continental surfaces
Daily field-scale time series of evapotranspiration are key to rationalize the use of water for irrigated agriculture
Evapotranspiration can be estimated as a residue of the surface energy balance equation, with land surface temperature as a major forcing variable
Timeliness is critical
Besides agriculture, many science and applications will benefit from high revisit & high resolution & high performance global surface temperature measurements
Challenges to deal with the thermal infrared signal: turbulence, directional anisotropy, pixel heterogeneity
Also technical challenges
Calibration & validation is challenging and will benefit from international synergies
TRISHNA is the frontrunner of this new generation of satellite missions
Contact: Philippe.Gamet@cnes.fr

## Slide 23
Additional slides

## Slide 24
Supporting public authorities
Supporting universities
European Science institutes and public authorities involved
in the preparation of TRISHNA
www.cnrs.fr
www.meteofrance.fr
www.cnes.fr
www.ofb.gouv.fr
www.ifremer.fr
www.inrae.fr
www.ird.fr
www.cerema.fr
www.uv.es www.uzh.ch
European Science institutes and public authorities involved
in the preparation of TRISHNA

## Slide 25
Indian Science institutes and public authorities involved
in the preparation of TRISHNA

## Slide 26
TRISHNA Production, timeliness and data distribution
Building a continuous time series of daily evapotranspiration at field scale (level 3 product)
Indo-french workshare
  Production
  Cataloguing
  Cross-validation
Objective: products available 12h after acquisition for vegetation water stress detection and irrigation management
Preparing a multi-mission time series with TRISHNA, LSTM, SBG, …
Total storage for 7 years of data
Generated products per year
Distributed products per day
14 PB
36 M
80 000
TRISHNA Production, timeliness and data distribution

## Slide 27
Land Surface Temperature Monitoring
Surface Biology and Geology
Dec 16, 2022
2026
2025
2029 & 2031
2028
Terrestrial Water Budget
Daily Evapotranspiration
Earth Observation missions in synergy
Earth Observation missions in synergy

## Slide 28
Building up the mission

## Slide 29
Multiple partnerships

## Slide 30
Preparing the mission on the ground (… and water, … and snow)
Berambadi: 11 SM+TIR monitoring stations (2022-) + UAV (2024)
Malegaon vineyard site, Maharashtra (2021-)
Berambadi Flux Tower (2023-)
Coast HF station
Saildrone
ECOSCOPA station
Waverider buoy

## Slide 31
TRISHNA Science Products to applications
Retrieval & Energy balance solutions
Assimilation to process & AI models
Assimilation to process models
Level 1 products
Geocorrected & radiometrically corrected clear-pixel TOA - Reflectances & Brightness temperatures
Atmospheric
correction
Urban microclimate
Cryosphere
Solid Earth
Coastal & Inland waters
Level 3 Products
Continuous all-sky evapotranspiration
Stress & productivity variables (*)
Level 2B water products (*)
Water quality
Water color
Level 2B land products
Vegetation variables
Radiation fluxes
Evaporation fluxes
Primary productivity (*)
Ecosystem stress &
water use
Level 2A products
Surface temperature
Surface emissivities
Surface reflectances
Atmospheric variables (AOD, water vapour)
Cloud mask
Downstream applications
(*) Under study, actual production to be confirmed

## Slide 32
Surface energy balance with TRISHNA inputs
Rn(T) = Rg.(1 – a) + ε.Ra – ε.σ.T4
Rn(T) = H(T) + LE(T) + G(T)
Net Radiation
Sensible Latent Ground
Surface energy balance
LEVEL 2